## Slide 1: Autonomous Driving Robot
Jow102 – MMP Mid-Project Demo

## Slide 2: Overview
The project’s main aim is to develop a robot that can detect and navigate lanes on a UK road while obeying current UK traffic laws.
There is also a secondary aim to have the robot be able to automatically detect and obey road signs (e.g., speed limits).

## Slide 3: Technologies Involved
Turtlebot3 – Waffle Pi (Robot)
ROS (Robot Control)
OpenCV (Image Processing)
Github (Version Control)

## Slide 4: Turtlebot3
Turtlebot3 is the robot which I have selected for use during this project. As this project is mainly about developing lane and road sign recognition, I did not require a complex robot.
Turtlebot3 has 3 different models: Burger, Waffle & Waffle Pi. I have chosen to use the Waffle Pi variant, as I do not require the use of the laser scanner that is available on the other models.
The robot for this project is simply required to have a forward facing camera, and the ability to drive around.

## Slide 5: ROS
ROS (Robot Operating System): While it’s name suggests that it is an ‘operating system’, it is actually just the middleware that is used to run the programs and control the robot.

## Slide 6: OpenCV
The image processing for the project is performed by making use of OpenCV. This library offers access to many image manipulation and processing tools.
The ‘CV_Bridge’ ROS library provides an interface between OpenCV and ROS. It allows the conversion of a ROS image message to an OpenCV image that can then be used for image processing.

## Slide 7: C++
The project is being developed in C++. I chose to use C++ over Python as I feel it provides a more in-depth library, and I am much more confident working in C++ compared to Python.

## Slide 8: Lane Detection Steps
Crop image – The top half of the image is not useful, and would only complicate the lane detection.
Convert to HSV colour space – Makes for easier colour masking
Colour Mask – Mask the image so only the white lines are visible.
Canny Edge Detector – Detects and highlights the edges of the lines.
HoughLinesP – Detects and draws lines along the detected edges.
Path Planning – Track best available Hough Lines and calculate centre of lane.

## Slide 9: Crop Image

## Slide 10: Convert to HSV

## Slide 11: Colour Mask

## Slide 12: Canny Edge Detection

## Slide 13: HoughLinesP & Path Planning

## Slide 14: Technical Issues Encountered
I had attempted a different approach to detecting the lines, by warping the image on either side of the robot to allow for easier identification of the lines. However this method quickly fell apart.
Tracking the most appropriate hough lines proved difficult, and still requires some fine tuning of the values for the edge detector and HoughLinesP. As well as some adjustments to the line selection algorithm.

## Slide 15: Intent For Rest of Project
Implement behaviour that drives robot along the planned path
Implement behaviour that will stop robot once it reaches the end of the road/give way. Behaviour should also automatically turn the robot onto the road.
Implement road sign recognition.