## Slide 1: Autonomous Driving Robot
Jow102 – MMP Mid-Project Demo

## Slide 2: Overview
The project’s main aim is to develop a robot that can detect and navigate lanes on a UK road while obeying current UK traffic laws.
There is also a secondary aim to have the robot be able to automatically detect and obey road signs (e.g., speed limits).

## Slide 3: Technologies Involved
Turtlebot3 – Waffle Pi (Robot)
ROS (Robot Control)
OpenCV (Image Processing)
Github (Version Control)

## Slide 4: Turtlebot3
Turtlebot3 is the robot which I have selected for use during this project. As this project is mainly about developing lane and road sign recognition, I did not require a complex robot.
Turtlebot3 has 3 different models: Burger, Waffle & Waffle Pi. I have chosen to use the Waffle Pi variant, as I do not require the use of the laser scanner that is available on the other models.
The robot for this project is simply required to have a forward facing camera, and the ability to drive around.

## Slide 5: ROS
ROS (Robot Operating System): While it’s name suggests that it is an ‘operating system’, it is actually just the middleware that is used to run the programs and control the robot.

## Slide 6: OpenCV
The image processing for the project is performed by making use of OpenCV. This library offers access to many image manipulation and processing tools.
The ‘CV_Bridge’ ROS library provides an interface between OpenCV and ROS. It allows the conversion of a ROS image message to an OpenCV image that can then be used for image processing.

## Slide 7: C++
The project is being developed in C++. I chose to use C++ over Python as I feel it provides a more in-depth library, and I am much more confident working in C++ compared to Python.

## Slide 8: Lane Detection Steps
Crop image – The top half of the image is not useful, and would only complicate the lane detection.
Convert to HSV colour space – Makes for easier colour masking
Colour Mask – Mask the image so only the white lines are visible.
Canny Edge Detector – Detects and highlights the edges of the lines.
HoughLinesP – Detects and draws lines along the detected edges.
Path Planning – Track best available Hough Lines and calculate centre of lane.

## Slide 9: Crop Image

## Slide 10: Convert to HSV

## Slide 11: Colour Mask

## Slide 12: Canny Edge Detection

## Slide 13: HoughLinesP & Path Planning